## Slide 1
The Internet Of Things
Introduction to what is the Internet of Things, why does it change the world where we live, what are the technologies behind the scene ?
How des it apply to your domain ?
Paul Pinault
Blog/contact : www.disk91.com
Twitter : @disk_91
YouTube: https://www.youtube.com/c/PaulPinault

## Slide 2
Helium is a blockchain for LoRaWan Distributed Global crowdsourced IoT Network
Author – Paul Pinault / Disk91.com

## Slide 3
Helium is a blockchain for LoRaWan Distributed Global crowdsourced IoT Network
Author – Paul Pinault / Disk91.com
Coverage is provided by a community of people instead of a company. Like TheThingsNetwork

## Slide 4
Helium is a blockchain for LoRaWan Distributed Global crowdsourced IoT Network
Author – Paul Pinault / Disk91.com
Investment on hardware is rewarded by a crypto token. Blockchain’s rules pilot the deployment and supports the main telecom industry processes.

## Slide 5
Helium is a blockchain for LoRaWan Distributed Global crowdsourced IoT Network
Author – Paul Pinault / Disk91.com
The network is global, it has started in North America, now covering Europe quickly and start in Asia.

## Slide 6
Helium is a blockchain for LoRaWan Distributed Global crowdsourced IoT Network
Author – Paul Pinault / Disk91.com
The networks supports multiple LoRa Network Servers (Routers) as private networks on top of the Gataways (Hotspot) public infrastructure.

## Slide 7
HELIUM
Is also crowdsourced IoT network, but it targets a different category of people to deploy the network. Instead of tech passionate, it target crypto investors.
Helium is an IoT network managed with a blockchain. Helium contributor are mining HNT tokens against coverage. Communication are billable with a flat and low price.
Basically, it is UBER + BITCOIN for Telecom industry
May 2020 3.025 HS
Nov 2020 12.477 HS
Feb 2021 18.700 HS
July 2021 77.100 HS
August 2021 100.000 HS
October 2021 220.000 HS
Nov. 2021 320.000 HS
Sept. 2022 954.940 HS
Feb. 2023 986.820 HS
Crowdsourced
Author – Paul Pinault / Disk91.com

## Slide 8
Author – Paul Pinault / Disk91.com
420K active hotspot in month, globally stable on the last 6 months.
July 2023 Status
Some mee-too blockchains try to take a part of it with Y connectors
Some big players leaves the game like bobcat
Hotspot have been made simpler, less need for maintenance, good stability.
Helium BUSINESS Usage per day in $ ($1 = 100k messages eq or 24Bytes)
Main console filtered due to gaming past month (add $50)
(drop due to normal packet purchasing (duplicates evolution))
About 10M packets processes per day for business applications
As part of it 60% is roaming packets for Telcos

## Slide 9
Helium is high density LoRaWan
Author – Paul Pinault / Disk91.com
New York
London
San Francisco
Paris
Amsterdam

## Slide 10
Helium at Clermont-Ferrand
Author – Paul Pinault / Disk91.com
EUROPE CONTEXT
CLERMONT-FD
COVERAGE MAP

## Slide 11
Helium distributed architecture
The HELIUM network is composed by hotspots. A Hotspot is a LoRaWan gateway associated to a Miner. A miner is lightweight and can run on a raspberry Pi. It is running in a docker container.
The miners are connected altogether over a P2P network. They are maintaining / running the blockchain.
Device communication passes through these different layers and are routed up to their specific Network Server. The distributed network supports multiple Network Servers. (Network Servers are centralized components in this architecture). Application servers works on helium as on any other Network Server. Nothing specific.
The data itself is not inside the blockchain.
DEVICES
HOTSPOT
P2P Network
Application Server
Users
Distributed IoT Network
Service Provider / User
Network Architecture (before HIP 71)
Author – Paul Pinault / Disk91.com
Network Server
Operator

## Slide 12
Helium Network Server Architecture
Helium have a geo-replicated routing infrastructure where all the hotspots push the received packets.
This infrastructure is verifying the packet, purchase it to the hotspost and route it to the right LNS.
LNS are running Chirpstack, open-source agnostic LoRaWan Server.
Devices and sessions needs to be declared in the Helium Routing service by the LNS. This requires API call to Helium Routing service (Config Service) on: Device Addition, Device Deletion, Device Session creation…
Specific open-source project has been created to support this ( see my github )
Author – Paul Pinault / Disk91.com
Network Server Architecture (current)
DEVICES
HOTSPOT
Users
Users
LNS
ROUTING
Hotspot Owners
Operator
APP SERVER
Private LNS
Nova Labs
Public LNS
Public LNS

## Slide 13
Author – Paul Pinault / Disk91.com
Hotspot transfers the packets to the nearest Helium router with geo-dns.
Routing Architecture
Router verify then transfer the packet to the LNS owning the packet
Helium Glue configure Helium routing infrastructure to correctly verify and route the packets.
v
USA
EUROPE
ASIA
Helium
Routing
Infrastructure
LNS (OUI 1)
LNS (OUI 2)
Chirpstack or other
Chirpstack or other
Helium
GLUE
Helium
Config Server

## Slide 14
Helium Routing Infrastructure
Author – Paul Pinault / Disk91.com
DEV EUI
APP EUI
APPKEY
HOTSPOT
CONFIG SERVICE
Route 1:
DEV EUI / APP EUI
DEV EUI / APP EUI
Route 2:
DEV EUI / APP EUI
DEV EUI / APP EUI
…
Route n:
…
PAQUET PURCHASER
Purchase valid DEV-EUI / APP-EUI
DEV-EUI
APPKEY
DEV ADR
APPSKEY
NTWSKEY
JOIN REQUEST
JOIN REQUEST
SEARCH
ROUTE
JOIN ACCEPT
LoRaWAN LNS
Helium Glue
LNS ( Chirpstack )
Detect ADD/DEL
DEVICES
Detect ADD/DEL
TENANTS
ADD/DEL
ROUTES
ADD/DEL
EUIS
ADD/DEL
SKFS
Detect Sessions
Pays
Packet
Helium router is searching for a route with a corresponding DEV-EUI / APP-EUI to accept the JOIN Request.
JOIN PROCESS
Helium Glue detects device addition & deletion to maintain the Config Service database with valid DEV-EUI/APP-EUI.
Helium Glue detects session creation to maintain the list of SKF (Session Key Filters) to the config Service. Basicaly the NTWSKEY list per DEVADR
Routes are managed by Helium Glue, can be global or per tenant. Route allows multiple LNS per OUI

## Slide 15
Helium Routing Infrastructure
Author – Paul Pinault / Disk91.com
HOTSPOT
CONFIG SERVICE
Route 1:
DEV ADR / NTWSKEY
DEV ADR / NTWSKEY
Route 2:
DEV ADR / NTWSKEY
DEV ADR / NTWSKEY
…
Route n:
…
PAQUET PURCHASER
Purchase valid DEVADR / NTWSKEY
DEVADR
NTWSKEY
APPSKEY
DEV ADR
APPSKEY
NTWSKEY
UPLINK REQUEST
UPLINK
SEARCH
ROUTE
DOWNLINK
LoRaWAN LNS
Helium Glue
LNS ( Chirpstack )
Count packets
& manage balance
ADD/DEL
EUIS
ADD/DEL
SKFS
Pays
Packet
Helium router is searching for a route with a corresponding DEV-ADR / NTWSKEY by verifying all signatures for the DEVADR.
UPLINK PROCESS
Valid packets are sent to LNS and paid to hotspots. Depends on max_copy route param, one or multiple packets are paid.
Helium Glue, in public usage, manage per device / account, packet balance. When a balance is reaching 0, the Glue will deactivate routes in config service.
Downlink are free of charge.

## Slide 16
Author – Paul Pinault / Disk91.com
Chirpstack tenant & device creation / deletion can be found in the PSQL Database.
Helium GLUE
Session Key are maintained in REDIS Database
Packet count & JOIN request can be detected with MQTT.
Chirpstack is per Region, not a global LNS. But we can dynamically update the region.
Helium ETL
Packet Forwarder
Hotspot
Lat/Long
S3
Helium Foundation
PoC & Reward data
Helium Legacy
Payload
Chirstack
Enriched Payload
With localization
HTTP Integration
Downlink handler

## Slide 17
Author – Paul Pinault / Disk91.com
Slide Deck
Content
Youtube Channel
WWW.DISK91.COM
GitHub Project